## Slide 1
FACLON LABS × OPEN BOOK EXTRACTS · LINE 1 OF 2 · CURRENT STATE
Kratom / MIT: Strong digital genealogy, thin process telemetry
Continuous-batch extraction with batch-level traceability from biomass lot to salt
1 Biomass lot
Receive and identify raw material
lot ID
source
weight
lot size ~14–17k kg
Tablet app · Cloud SQL
2 Pretreatment / extraction
Pull alkaloids out with solvent (heptane)
tank level
pump/valve state
cycle & drain timing
flow/pressure
Beckhoff PLC + HMI
3 Extraction tote
Hold extract, carry batch identity forward
tote ID
source lot link
volume
transfer time
Cloud SQL genealogy
4 Crystallization batch
Cool and adjust to crystallize freebase; yield-critical
pH curve
internal/jacket temp
base dosing
hold time
5 Freebase drum
Weigh and package freebase as a traceable unit
gross/tare/net
drum ID
material identity
6 Acetate salt run
Convert freebase to the finished salt
input weights
salt conversion weights
drum link
7 QC / inventory
Verify spec, release to stock
HPLC assays
external COAs
inventory transactions
Linkage to validate
In-house HPLC · COAs · Acumatica
4
Heptane solvent mass balance — not measured today
lot
tote
tote
batch
drum
run
3
5
7
7
7
PLC data not stored
PLC data not stored
DIGITAL BACKBONE
Browser / tablet apps
→
Google Cloud Run
→
Cloud SQL (PostgreSQL)
→
Cloud Storage
Acumatica (ERP)
HOW KEY DATA IS CAPTURED TODAY
Structured digital
Manually entered
Displayed, not retained
Paper record
Not measured
#
Numbered badges = Faclon opportunity priority (from pre-read)
BUSINESS QUESTION THIS LINE SHOULD ANSWER
“Where is heptane actually being lost, and what is solvent loss per kg of finished MIT?”
Current state per OBX Operations & Data Pre-Read (Sept 2026). To be validated onsite.
Notes: Read left to right: biomass lot to QC release. Chip colour in each card corner = how that step's key data is captured today. Teal risers show the steps whose data already lands in Cloud SQL / Acumatica; the dotted risers at extraction and crystallization show PLC data that stays on the Beckhoff HMI. The hatched red region is the heptane mass-balance gap across extraction and LLE (opportunity 4). Onsite: confirm which PLC tags exist, whether any history is kept locally, and how freebase / salt weights reach the system.

## Slide 2
FACLON LABS × OPEN BOOK EXTRACTS · LINE 2 OF 2 · CURRENT STATE
Bulk Cannabinoids: Well-controlled on paper, ready for eBPR
Batch distillation, crystallization and conversion run on controlled paper BPRs and local equipment displays
1 Crude / WDC
Receive crude oil and open the batch
batch/lot ID
input mass
material identity
Controlled BPR · Acumatica
2 1M WFE deterp
First wiped-film pass to strip light terpenes
vacuum
temperature set/actual
feed & run-off
chiller
2-hour snapshot
FOR-BIP-009
3 2M WFE distillation / FSD
Second pass to distill the cannabinoid fraction
wiper/feed
vacuum
temp
evaporator & condenser
output mass
SOP-BIP-004 vs 006: confirm governing SOP
FOR-BIP-010
BRANCH A · CBD ISOLATE
4a CBD isolation (ISO-A to ISO-E)
Crystallize CBD isolate
heptane charge
internal & jacket temp
cool to −18 °C
tray timing
FOR-BIP-004
BRANCH B · DERIVATIVE REACTION (E.G., DELTA-8)
4b Derivative reaction (RXN-1 / RXN-3)
Chemically convert to Delta-8
PTSA & heptane
50–55 °C pre-acid
exotherm
85–95 °C cook
3 washes
FOR-BIP-003
5 Wash / final purification / drying
Filter, wash and dry to spec
rinse events
filtration time
vacuum
oven temp & time
6 QC / inventory
Verify spec, release to stock
assays
COAs
inventory transactions
In-house lab · COAs · Acumatica
6
6
2
Bulk electronic batch records · recommended hybrid eBPR, paper to digital
Auto-populate from equipment
VFDs, controllers, gauges, temperature curves
Operator attests
Critical additions, visual judgment, exceptions, handoffs
Quality controls
Template control, audit trail, e-signatures, retention
2-hour snapshots → continuous history
HOW KEY DATA IS CAPTURED TODAY
Structured digital
Manually entered
Displayed, not retained
Paper record
Not measured
#
Numbered badges = Faclon opportunity priority (from pre-read)
BUSINESS QUESTION THIS LINE SHOULD ANSWER
“Which WFE operating conditions are associated with yield or quality variation?”
Current state per OBX Operations & Data Pre-Read (Sept 2026). To be validated onsite.
Notes: Every step on this line is governed by a controlled paper BPR, so the chips are almost all grey: the controls are solid, the data is on paper. WFE passes (steps 2 and 3, opportunity 6) are logged as 2-hour snapshots from local displays. After step 3 the batch goes either to CBD isolation or to the derivative reaction, then rejoins for wash, purification and drying. The lower band is the hybrid eBPR approach (opportunity 2): equipment auto-populates, operators attest, Quality keeps template control and signatures. Onsite: confirm whether SOP-BIP-004 or 006 governs the 2M pass, and which WFE / oven controllers expose data.